## Slide 1: Modern Systems What Are FPGAs and Why Should You Care
Slides adapted from: Sang-Woo Jun, UCI
FPGA Workshop 3-4 June, Dr. Muhammad Yasin

## Slide 2: What Are FPGAs
Field-Programmable Gate Array
Can be configured to act like any circuit – More later!
Can do many things, but we focus on computation acceleration

## Slide 3: FPGAs Come In Many Forms
PCIe-Attached
CPU Integrated
In-Network
In-Storage

## Slide 4: How Is It Different From CPU/GPUs
GPU – The other major accelerator
CPU/GPU hardware is fixed
  “General purpose”
  we write programs (sequence of instructions) for them
FPGA hardware is not fixed
  “Special purpose”
  Hardware can be whatever we want
  Will our hardware require/support software? Maybe!
Optimized hardware is very efficient
  GPU-level performance**
  10x power efficiency (300 W vs 30 W)

## Slide 5: Analogy
“The Z-Berry”
“Experimental Investigations on Radiation Characteristics of IC Chips”
benryves.com “Z80 Computer”
CPU/GPU comes with fixed circuits
FPGA gives you a big bag of components
To build whatever
Shadi Soundation: Homebrew 4 bit CPU
Could be a CPU/GPU!

## Slide 6: Fine-Grained Parallelism of Special-Purpose Circuits
Example -- Calculating gravitational force:
8 instructions on a CPU → 8 cycles**
Much fewer cycles on a special purpose circuit
A = G × m1
B = A × m2
C = x1 - x2
D = C2
E = y1 - y2
F = E2
G = D + F
Ret = B / G
A = G × m1 × m2
B = (x1 - x2)2
C = (y1 - y2)2
D = B + C
Ret = B / G
4 cycles with basic operations
3 cycles with compound operations
Ret = (G × m1 × m2) / ((x1 - x2)2 + (y1 - y2)2)
1 cycle with even further compound operations
May slow down clock

## Slide 7: Coarse-Grained Parallelism of Special-Purpose Circuits
Typical unit of parallelism for general-purpose units are threads ~= cores
Special-purpose processing units can also be replicated for parallelism
  Large, complex processing units: Few can fit in chip
  Small, simple processing units: Many can fit in chip
Only generates hardware useful for the application
  Instruction? Decoding? Cache? Coherence?

## Slide 8: How Is It Different From ASICs
ASIC (Application-Specific Integrated Circuit)
  Special chip purpose-built for an application
  E.g., ASIC bitcoin miner, Intel neural network accelerator
  Function cannot be changed once expensively built
+ FPGAs can be field-programmed
  Function can be changed completely whenever
  FPGA fabric emulates custom circuits
- Emulated circuits are not as efficient as bare-metal
  ~10x performance (larger circuits, faster clock)
  ~10x power efficiency

## Slide 9: Basic FPGA Architecture
“Configurable logic block (CLB)”
Programmable interconnect
I/O block
6-Input
Look-Up
Table
FF
Latch
Programmable
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Ex) 2-LUT for “AND”
~
Sequential circuit
construction

## Slide 10: Basic FPGA Architecture – DSP Blocks
CLBs act as gates – Many needed to implement high-level logic
Arithmetic operation provided as efficient ALU blocks
  “Digital Signal Processing (DSP) blocks”
  Each block provides an adder + multiplier
“DSP block”
×
+/-

## Slide 11: Basic FPGA Architecture – Block RAM
CLB can act as flip-flops
  (~1 bit/block) – tiny!
Some on-chip SRAM provided as blocks
  ~18/36 Kbit/block, MBs per chip
  Massively parallel access to data → multi-TB/s bandwidth
“Block RAM”

## Slide 12: Basic FPGA Architecture – Hard Cores
Some functions are provided as efficient, non-configurable “hard cores”
  Multi-core ARM cores (“Zynq” series)
  Multi-Gigabit Transceivers
  PCIe/Ethernet PHY
  Memory controllers
  …
ARM
PCIe
Ethernet
Memory

## Slide 13: Example Accelerator Card Architecture
PCIe
FPGA
DRAM
DRAM
1GbE
FMC
40GbE
“FPGA Mezzanine Card” Expansion
  Network Ports, Memory, Storage, PCIe, …
General-Purpose I/O Pins
Multi-Gigabit Transceivers

## Slide 14: Example Accelerator Card (VCU108)

## Slide 15: Programming FPGAs
Languages and tools overlap with ASIC/VLSI design
FPGAs for acceleration typically done with either
  Hardware Description Languages (HDL): Register-Transfer Level (RTL) languages
  High-Level Synthesis: Compiler translates software programming languages to RTL
RTL models a circuit using:
  Registers (state), and
  Combinational logic (computation)

## Slide 16: Hardware Description Language
Software programming languages: Describes process
Hardware description languages: Describes structure
FIFO#(Float) input_queue <- mkFIFO;
FIFO#(Float) output_queue <- mkFIFO;
Reg#(Float) factor <- mkReg;
FloatMultIfc mult <- mkFloatMult;
rule in;
mult.enq(factor, input_queue.first);
input_queue.deq;
endrule
rule out;
ret <- mult.result;
output_queue.enq(ret);
endrule
std::queue<float> input_queue;
std::queue<float> output_queue;
float factor;
while (true) {
if ( !input_queue.empty() ) {
ret = input_queue.front() * factor;
output_queue.push(ret)
input_queue.pop();
}
}
Exists in memory
Exists on chip
Creates
circuits
Instructions
For CPU

## Slide 17: Major Hardware Description Languages
Verilog: Most widely used in industry
  Relatively low-level language supported by everyone
Chisel – Compiles to Verilog
  Relatively high-level language from Berkeley
  Embedded in the Scala programming language
  Prominently used in RISC-V development (Rocket core, etc)
Bluespec – Compiles to Verilog
  Relatively high-level language from MIT
  Supports types, interfaces, etc
  Also active RISC-V development (Piccolo, etc)

## Slide 18: High-Level Synthesis
Compiler translates software programming languages to RTL
High-Level Synthesis compiler from Xilinx, Altera/Intel
  Compiles C/C++, annotated with #pragma’s into RTL
  Theory/history behind it is a complex can of worms we won’t go into
  Personal experience: needs to be HEAVILY annotated to get performance
  Anecdote: Naïve RISC-V in Vivado HLS achieves IPC of 0.0002 [1], 0.04 after optimizations [2]
OpenCL
  Inherently parallel language more efficiently translated to hardware
  Stable software interface
[1] http://msyksphinz.hatenablog.com/entry/2019/02/20/040000
[2] http://msyksphinz.hatenablog.com/entry/2019/02/27/040000

## Slide 19: FPGA Compilation Toolchain
High-Level
HDL Code
Language
Compiler
Verilog/
VHDL
Synthesize
Netlist
Map/
Place/
Route
Bitfile
High-level language vendor tool
FPGA Vendor toolchain (Few open source)
Constraint
File
“Which transceiver instance should
top_transceiver_01 map to?”
And so, so much more…
Cycle-level
Simulation
Functional
Simulation

## Slide 20: Programming/Using an FPGA Accelerator
Bitfile is programmed to FPGA over “JTAG” interface
  Typically used over USB cable
  Supports FPGA programming, limited debugging access, etc
PCIe-attached FPGA accelerator card is typically used similarly to GPUs
  Program FPGA, execute software
  Software copies data to FPGA board, notify FPGA -> FPGA logic performs computations -> Software copies data back from FPGA
FPGA flexibility gives immense freedom of usage patterns
  Streaming, coherent memory, …

## Slide 21: Partial Reconfiguration
FPGA
Sub-components
Parts of the FPGA can be swapped out dynamically without turning off FPGA
  Physical area is drawn on chip
Used in Amazon F1, etc
Toolchain support for isolation

## Slide 22: FPGAs In The Cloud
Amazon EC2 F1 instance (1 – 4 FPGAs)
Microsoft Azure, etc…

## Slide 23: FPGA vs CPU vs GPU vs ASIC

## Slide 24: GPU vs FPGA

## Slide 25: GPU vs FPGA
https://www.bertendsp.com/gpu-vs-fpga-performance-comparison/

## Slide 26: FPGAs in space

## Slide 27: FPGAs in Defense
source: Xilinx Inc

## Slide 28: Selection criteria
https://www.mobilityengineeringtech.com/component/content/article/adt/pub/features/articles/6332